## Slide 1: So you want to put a neural network on an airplane…
Darren Cofer | Principal Fellow
AI Assurance workshop
10 August 2023
Notes: Challenges
Certification guidance
Applications

## Slide 2: What could possibly go wrong?
https://twitter.com/andyweedman/
status/1382459653863378944
https://twitter.com/Cbiggs90/status/1519821916189741057
https://www.latimes.com/business/story/2019-09-03/tesla-was-on-autopilot-when-it-hit-culver-city-fire-truck-ntsb-finds
brake

## Slide 3: What could possibly go wrong?
Aviation Edition
ENGINE FAULT AT 110 KTS
End of runway
V1
Engine fault
Reject
NN trained using reinforcement learning to make reject takeoff (RTO) decision for 737 aircraft (DARPA Assured Autonomy project)

## Slide 5: Why?
Increasing automation of pilot tasks
  Recovery and continued increase of demand for commercial air travel
  Supply chain demands for shipping goods and materials by cargo carriers
  New demands for transportation (both speed and capacity) in high-density urban areas
  Shortage of trained pilots for the foreseeable future
  eMCO, RCO, SPO… full autonomy?
Save computational resources in onboard embedded systems
  Gigantic look-up tables (memory)
  Complex optimization functions (CPU time)

## Slide 6: What’s different with ML?
FAA has determined that AI/ML technologies are “new and novel”
This means that they cannot be approved based on existing standards and means of compliance
Approval can be obtained using the Issue Paper process in accordance with AC 20-166A to determine acceptable Method of Compliance
Why can’t we just do what we’ve always done for certification?

## Slide 7: Assurance Challenges for Machine Learning
https://xkcd.com/1838/
Requirements
  ML functional requirements are often imprecise (image classification)
  Large labeled training/test datasets are more important
Verification
  Traditional assurance (DO-178C) relies on requirements-based test cases with structural coverage metrics to assess completeness
Implementation
  Design intent usually cannot be inferred from examination of design artifacts
  Neither design elements nor implementation code are traceable to requirements
  Structural coverage metrics are unable to detect unintended behavior in response to novel inputs
Requirements
Implementation
Verification

## Slide 8: Certification Challenges
Training and Test Data
Model Design and Training
Machine
Learning Magic
ML Model
DO-331?
Gap
Mostly
Unchanged
Mostly
Unchanged
Means of compliance with airworthiness regulations

## Slide 9: EASA Approach to ML

## Slide 10: FAA Approach to ML
Technology is evolving, standardization is premature
Evaluate specific projects from applicants

## Slide 11: SAE G34 / EUROCAE WG-114
Learning Process
  Use subsystem requirements to define Operational Design Domain (ODD) and training/test datasets
  Data generation/management
  Data is complete and representative relative to ODD
  Model training to achieve performance target
Verification of Trained Model
  Show absence of unintended behavior
  Generalization
  Stability
  Robustness
Inference Model Implementation
  Implement model functionality using traditional methods
  Verification using traditional methods
Inference Model Integration/Verification
  Show that implementation of inference model preserves properties of trained model
  Requirements verification
  Performance verification
  Robustness on target hardware
  Compatibility with target hardware
ARP6983 : Process Standard for Development and Certification / Approval of Aeronautical Safety-Related Products Implementing AI
Directly related to unintended behavior

## Slide 12: Unintended behaviors
Generalization
  How does system respond to novel/unexpected inputs that were not included in training dataset?
  In ODD but “between” concrete training points
Stability
  How does system respond to perturbations around training data points?
  Can small input disturbances result in large output deviations?
  Related to adversarial inputs
Robustness
  How does system respond to inputs near boundary of ODD?
  Similar to abnormal inputs (robustness test cases in DO-178C)
https://www.codingninjas.com/codestudio/library/bias-variance-tradeoff
Performance vs. Generalization

## Slide 13: Aviation ML Applications
COMPLEXITY
CRITICALITY
Optimal Flight Level
Fuel Measurement
ACAS-Xu Collision Avoidance
Pilot Alertness
(Warning)
Detect & Avoid
Visual Landing
Equipment Health Monitoring
Planning input to Pilots (Advisory)
Pilot Alertness (SPO)
VISION/PERCEPTION BASED SYSTEMS
SIMPLE OPERATIONAL DOMAIN
LOW IMPACT OF FAILURE
Perception is a strong point for ML/DNN, but also hardest to verify (size, requirements)
https://xkcd.com/1425/
ML not necessary (there are existing alternatives) but is used to save memory or compute time
Formal methods can be used to demonstrate absence of unintended functionality
SCALE-UP
Runway Overrun Warning

## Slide 14: First Steps : DAL D
Software is a “black box”
Testing to show that software meets its requirements
  Very little about implementation details
  Nothing related to unintended function
What else might be needed?
  Operational Design Domain (ODD)
  Training data set
  Verification data set
  Basic architecture (e.g., 3-layer feed-forward neural network with tanh activation functions, trained with PyTorch)
Black
Box

## Slide 15: First Steps : Simple NN
Criticality up to DAL A supported
Limited to NN with “simple” ODD (or “small” model)
  Small number of well-defined scalar-valued sensor inputs with max/min range
  I.e., not images
What else might be needed?
  Full learning assurance process, similar to AS6983 MLDL or EASA First Usable Guidance (for DAL A-C anyway)
  Rigorous Data Management Process
  Demonstrations of generalization, stability, robustness
  Justification for absence of unintended behavior/function (using formal methods, traditional mathematical reasoning, or extremely dense training/testing data sets)
Complex NN will not yet be able to satisfy these objectives
Detailed
Learning
Assurance
Process
(MLDL)

## Slide 16: Summary
Machine learning presents unique assurance challenges in the aviation environment (mostly related to unintended behaviors)
FAA and EASA are preparing for initial proposals/applications, but with very different approaches
The SAE G34 / EUROCAE WG114 joint committee is moving forward to produce industry consensus certification guidance that is intended to address the challenges posed by AI/ML, enabling its use in increasingly autonomous aircraft
High complexity ML functions (vision/perception) will continue to be a challenge in applications that require higher levels of assurance
But we can make progress now on simple / low criticality ML function

## Slide 17
Unintended Behavior in Learning-Enabled Systems: Detecting the Unknown Unknowns
D. Cofer. Digital Avionics Systems Conference (DASC), October 2021
Flight Test of a Collision Avoidance Neural Network with Run-Time Assurance
D. Cofer, R. Sattigeri, I. Amundson, J. Babar, S. Hasan, E. Smith, K. Nukala, D. Osipychev, M. Moser, J. Paunicka, D. Margineantu, L. Timmerman, J. Stringfield. Digital Avionics Systems Conference (DASC), September 2022.
Formal Methods use for Learning Assurance (ForMuLA)
M. Baleani, A. Clavière, D. Cofer, E. DeWind, L. Di Guglielmo, O. Ferrante, G. Gentile, D. Kirov, D. Larsen, L. Mangeruca, S. Fulvio Rollini, G. Cima, R. Schneider H. Semde, G. Soudain
Collins Aerospace / EASA IPC Report
Loonwerks.com